## Slide 1: SUMMARY OF MOSAIX CHARATERIZATION TALK EPIC COLLABORATION MEETING
Ivan Amos Cali, Leyre Flores, Gian Michele Innocenti, Anhelina Kostina, Lukas Tomasek
MIT group meeting
31/01/2025

## Slide 2
Slide by Gregor Eberwein

## Slide 3
Slide by Gregor Eberwein

## Slide 4
MIT RESPONSIBILITIES FOR SVT
Jelena is part of the ALICE ITS3 design team of a 27 cm long MAPS detector
SVT has in place an agreement with ALICE ITS3 in order to reuse and repurpose its MAPS detectors
  They will share the design files and the technology will be adapted to ePIC needs
MIT (us) are responsible of SVT WP2 (testing and characterisation)
Wafer probe-based characterization has emerged as the most efficient testing strategy for both SVT and ITS3

## Slide 5
WHAT IS WAFER PROBING AND WHY?
What is wafer probing?
  A wafer probing is a system used for electrical testing of the wafers of individual chips
    Power on, read/write register, analogue and digital scans, threshold etc.
Why do we want to use it as main characterization technique?
  It makes the process faster and more efficient
  → It is effectively the only viable solution for the SVT (~200 wafers to test)
Is this not done for most of our detectors?
  Yes it is a technique that has been used for years but at MIT we want to go one step further a try a new technique that allows to get data at high-speeds, so far all the testing was at < 300 Mbps

## Slide 6
A DEDICATED WAFER PROBER @ CERN
VERTICAL PROBE CARD
CANTILEVER PROBE CARD
HIGH SPEED
LOW SPEED

## Slide 7
A DEDICATED WAFER PROBER @ CERN
MPI TS-3500 SE
Installed at the DSF lab
Wafer wallet for fully automatized testing
Multiple cameras available
  Must for vertical probing
Capable to load 300 mm wafers
Micro-holes for accurate placing of ultra thin wafers

## Slide 8
PROBE CAR SETUP AND WAFER MAP GENARATION
Probe card holder and alignment
Inclination adjust wheel
Screws for z position
Rails for X and Y
Wafer map generation

## Slide 9
PROBE TO PAD ALIGNMENT
Topography maps
Pobe To Pad Alignment training (PTPA)
Uses light reflection to calculate the differences in heights across the wafer using the specified dies
Training procedure using marker, pads and tips to align needles to pads in X, Y and Z

## Slide 10
DEVELOPING AUTOMATIC TESTING
Goal of sharing the projects and scripts with all the institutes involved in wafer probing testing
  Github repository: https://github.com/SVT-WP2/MITWP1/tree/main
Currently to main folders:
  Python projects: Sentio Software Remote commands scripts to operate the WP
  Scripts: Bash scripts that allow to test a full system including DAQ, PS and WP commands
All the automatization process has been done using the features of vertical probing
Code snippet from the Scripts

## Slide 11
WORKFLOW WAFER PROBE TESTING
New wafer installation
Manual Sentio Project Setup
Wafer alignment
Wafer map generation
PTPA training
Topography
Wafer_name_project
Probe card adjustments
MANUAL SETUP ONLY ONCE PER WAFER TYPE
Automatization scripts
Electrical Tests
Wafer_name_project
Readout and control HW
WP remote control
Analysis of results
Includes PS control
AUTOMATIC TESTING
~ 30 MIN
per wafer family
Few min to load wafer
+ few sec per die

## Slide 12
MIT group meeting
FIRST RESULSTS AND MACHINE VALIDATION
Tested all 25 babyMOSS top unit in the wafer in 25 minutes with ~identical results to ALICE using our new tools
  Electrical tests as Digital Scan, PowerOnTest, Registers scan
W124A 3-1 HIT MAP
W124A 3-3 NOISY PIXELS
ALICE ITS3 RESULTS
SVT RESULTS

## Slide 13
MIT group meeting
CURRENT STATUS OF THE SETUP

## Slide 14
MIT group meeting
CURRENT STATUS OF THE SETUP