## Slide 1: Major limitations of existing fixed field ring accelerators
Malek HAJ TAHAR
Paul Scherrer Institut
Snowmass’21 Workshop on High Power Cyclotrons
07 September 2021

## Slide 2: Disclaimer
Since a large number of different fixed field accelerator concepts exist, attention will be focused on the methods and aspects that are generally used (operating) nowadays.
It should be noted that this approach cannot give a complete overview of the field and some conclusions have exceptions.
The limitations discussed are so called because the focus is on what limits the achievable currents.

## Slide 3: Overview
Magnetic field limitations
Beam extraction limitations
RF considerations
Summary

## Slide 4: Livingston chart
1 μA
10 μA
100 μA
1 mA
10 mA
PSI 590 MeV ring
TRIUMF 520 MeV ring
Daeδalus
UCLA 60
PSI Proscan 250
IBA C70
Berkeley CP42
ORIC 42
IBA C10
TR 30
UW 50
Gatchina SC 1000
Curie SC 200
CERN SC 600
Dubna SC 700
SC = Synchro-Cyclotron
Major RF upgrades
Nevis SC 570
The numbers displayed represent the extraction energy in MeV
Livingston chart for beam intensity showing an increase by nearly one order of magnitude per decade since the 70s.
Tremendous effort to tune the machine..

## Slide 5
To facilitate the discussion, we focus on 2 concepts aiming for High Intensity, CW vs pulsed ...

## Slide 6
Example of several closed orbits in the PSI 590 MeV ring cyclotron in Villigen (constant step size in energy).
Example of several closed orbits for the KURRI 150 MeV scaling FFA at Kyoto. First beam in 2006.
Separated Sector Cyclotrons
Scaling FFA
Over 40 years of upgrades!
Reinvented by Y. Mori et al
In ~ 2000

## Slide 7: Magnet considerations
In an FFA/cyclotron, magnetic field is a complicated function in radial and azimuthal coordinates such as:
  For a cyclotron, and the average field index
  For a scaling FFA, where
; is the average field at fixed radius and is the average field index
In practice, it is difficult to build magnets with large field index exactly as prescribed (case of scaling FFA and cyclotrons approaching the GeV level):
  Proximity of the magnets
  Variable gap size
  Closed orbits distortion  path length + effective focusing differ in the neighbourhood of each orbit.
 Field errors
For FFA, orbit compression often desired  large k values required  horizontal tune generally larger than the vertical one. FFA magnets are generally smaller than cyclotron magnets with k >> 1.

## Slide 8
2 types of field errors that can limit their performance:
- dipole field errors
- gradient field errors

## Slide 9: Dipole field errors
The concept of isochronism excludes phase stability
 severe tolerances on magnetic field errors.
Constraint: the beam phase shall remain within , in order to accelerate it to full energy.
Level of isochronism generally aimed: 0.01 %.
Recalling that , it results that a field change of prohibits acceleration to full energy for the PSI 590 MeV ring for instance [ref 1]
B is the average field per turn.
RF phase of the accelerated particles as a function of radius for the 590 MeV PSI cyclotron. The magnetic field is isochronous to between 75 and 580 MeV without exciting any trim coil [ref 1]

## Slide 10: Dipole field errors-Remedies
Layout of PSI ring cyclotron with trim coils (18) placed on top of the main magnets’ pole plates [ref 5, 6, 7]
Fine shimming of pole edges/adding field clamps [ref 2]
Correction trim coils to ease the beam extraction and overcome some resonance crossings [ref 3]
  8-fold symmetry reduced by a factor of 2.
Harmonic coils to correct coupling resonances [ref 4]
Coarse isochronism Main coils individually excitable

## Slide 11: Gradient field errors
Why gradient field errors matter (azimuthally)?
The field index is constant everywhere except in the interaction region between the F and D magnets:
  No steel return yoke employed to facilitate the injection/extraction [ref 9]  the flux of the F magnet returns through the D magnet and alters its gradient (problem inexistent for booster ring).
Map of the field index in the D and F magnets [ref 8]
Larger variations at low energies
Layout of the KURNS 150 MeV scaling FFA (larger of the two rings)

## Slide 12: Gradient field errors  Resonances
Lessons learned: Making average k constant insufficient to guarantee a fixed tune machine. Scaling as originally prescribed must be valid locally as well as globally.
Tune excursion due to scaling imperfections is and to the FD ratio of the magnet.
Even for a cyclotron, gradient field errors will lead to strong tune variations and are often introduced at extraction to enhance the turn separation. Nearly negligible when rapidly crossed.
Betatron tunes from 11 to 100 MeV (left to right) at the KURNS 150 MeV FFA [ref 8, 9, 10].
Average forces applied to the beam (cyclotron regime, no spiral angle assumed)
Deviations around the mean values of these forces
(AG focusing)
Edge focusing
;
1 ms
20 ms

## Slide 13: Gradient field errors-Remedies
Three possible remedies to field errors:
Field clamps: Shall primarily affect the edge focusing (vertical tunes)
Tuning can be tedious (combined function magnets).
Both quantities to adjust (revolution time, tunes) are average quantities.
Same approach applies both for cyclotrons and scaling FFA
Courtesy Yuhi Waga
Kyushu radial scaling FFA
RACCAM spiral scaling FFA [ref 11]
Courtesy Thomas Planche

## Slide 14: Gradient field errors-Remedies
Three possible remedies to field errors:
Field clamps: Shall primarily affect the edge focusing (vertical tunes)
Flux return yokes
Tuning can be tedious (combined function magnets).
Both quantities to fix (revolution time, tunes) are average quantities.
Same approach applies both for cyclotrons and scaling FFA
Courtesy Yuhi Waga

## Slide 15: Gradient field errors-Remedies
Three possible remedies to field errors:
Field clamps: Shall primarily affect the edge focusing (vertical tunes)
Flux return yokes
Trim coils: Aim to fix the tune by replacing the N-fold symmetry machine with N/2 or even N/3 symmetry.
Tuning can be tedious (combined function magnets).
Both quantities to fix (revolution time, tunes) are average quantities.
Same approach applies both for cyclotrons and scaling FFA
Ways to mitigate magnetic field imperfections shall be considered in the preliminary design phase of the accelerator.
Controls the monotonic behavior

## Slide 16
Beam dynamics are driven by the need to extract the highest current with low losses.

## Slide 17: Beam Extraction challenges
For the same radius and energy at extraction, a fixed field alternating gradient will have a smaller turn separation due to its larger k value aiming for a more compact orbit excursion.
Above formula valid for a pencil beam only i.e. for a vanishing beam size.
Stripping H2+ or H- ions to circumvent the problem (see talks by T. Planche and L. Calabretta), yet the cost is a larger machine.
Next, the focus will be on the single turn extraction challenges
R is the radius at extraction
For a cyclotron
For a scaling FFA, k is constant
is the energy gain per turn
Radial turn separation at extraction valid for any fixed field ring accelerator:

## Slide 18: Beam Extraction challenges: Energy dependence
How to overcome?
Observation: Small turn separation at extraction.
Turn separation for various FFA concepts

## Slide 19: Beam Extraction challenges: Energy dependence
Observation: Small turn separation at extraction.
Horizontal tunes as a function of turn number for the PSI ring cyclotron
Last 7 turns
How to overcome?
Lower the horizontal tunes at the extraction region
Turn separation for various FFA concepts

## Slide 20: Beam Extraction challenges: Energy dependence
How to overcome?
Lower the horizontal tunes at the extraction region
Inject the beam off-center
Optimize the dispersion function at injection (to reduce the contribution of the momentum spread at extraction)
   Wins a factor 3 in turn separation [ref 12]
Flat-top system to further reduce the energy spread
Bunching the beam at injection
Collimation to clean the beam tails (several steps)
Increase the energy gain per turn RF upgrades
Observation: Small turn separation at extraction.
Turn separation for various FFA concepts

## Slide 21: Beam Extraction challenges: Intensity dependence
Radial probe measurement at the extraction region of the PSI 590 MeV cyclotron: Normalized bunch intensity. Experiment in the frame of the HIMB project by J. Snuverink, D. Reggiani, C. Baumgarten, H. Zhang and M. Haj Tahar.
Measured turn separation guaranteeing 99.98 % extraction efficiency (clean region where the inner electrode can be placed safely).
14 mm
Extraction septum
The determining factor for low losses is the ratio of the width of the beam to the turn separation at extraction [ref 13].
Operational experience at PSI proved that beam losses could be kept below 0.02 %
 Wider beam to accommodate more charge
Fine-tuning

## Slide 22
Question: Large magnets are less tolerant to imperfections?
“Compactness is generally not an advantage for high intensity”
Mike Seidel [ref 14]
Yet, for a hospital environment, compactness is a must …

## Slide 23: Summary
Concept | Energy reach | Intensity reach | Operation mode | Orbit excursion/size | Peak current | Intensity limitations
Cyclotron | <= 1 GeV | mA level PSI: 2.4 mA | CW | Large | Low | Limited by turn separation at extraction
Synchro-Cyclotron | ~ 1GeV | μA level Dubna: 25 μA | Pulsed mode ( kHz) | Large | Low | Limited by RF capabilities
FFA (scaling) | No fundamental limit – AG | nA level KURNS: ~ 10 nA (ADS constraint) | Pulsed mode ( kHz) | Small | High-large acceptance | Limited by RF capabilities + resonances
Concept | Energy reach | Intensity reach | Operation mode | Orbit excursion/size | Peak current | Intensity limitations
Cyclotron | <= 1 GeV | mA level PSI: 2.4 mA | CW | Large | Low | Limited by turn separation at extraction
Synchro-Cyclotron | ~ 1GeV | μA level Dubna: 25 μA |  | Large | Low | Limited by RF capabilities
FFA (scaling) | No fundamental limit – AG | nA level KURNS: ~ 10 nA (ADS constraint) |  | Small | High-large acceptance | Limited by RF capabilities + resonances
“The ion current from a synchro-cyclotron is typically 1 % of that from a classical cyclotron under comparable conditions”
Above the GeV level, FFA shall be the obvious way to deliver high intensity beams (for fixed field rings). Yet, demonstrating such a capability is eagerly awaited for medium energy concepts.
M.K. Craddock and K.R. Symon [ref 15]
State-of-the-art of fixed field light ion accelerators

## Slide 24: Acknowledgements
Special thanks go to:
Davide Reggiani, Jochem Snuverink, Andreas Adelmann, Christian Baumgarten and Hui Zhang from PSI for all useful discussions regarding cyclotrons.
François Méot, Shinji Machida, Scott Berg and Dejan Trbojevic for all discussions related to fixed field accelerators in general.
All members of the KURNS group in Japan, specifically Yoshihiro Ishi and Yoshiharu Mori for the stimulating work on the scaling FFA.

## Slide 25: Reference lists
[1] The S.I.N. Ring Cyclotron after One Year of Operation (cern.ch)
[2] Magnets for cyclotrons
[3] Towards quantitative simulations of high power proton cyclotrons
[4] Correction of nur=3/2 resonance in triumf cyclotron
[5] S. Adam and W. Joho, PSI Technical Report No. TM-11-13, 1974.
[6] Matching of turn pattern measurements for cyclotrons using multiobjective optimization (aps.org)
[7] Measurements of the Beam Phase Response to Correcting Magnetic Fields in PSI Cyclotrons (cern.ch)
[8] Tune compensation in nearly scaling fixed field alternating gradient accelerators (aps.org)
[9] Practical Betatron Tune Behavior During Acceleration in Scaling FFAG Rings at KURNS (cern.ch)

## Slide 26
[10] Progress on Simulation of Fixed Field Alternating Gradient Accelerators (cern.ch)
[11] 3-D magnetic calculation methods for SPIRAL scaling FFAG magnet design (in2p3.fr)
[12] The feasibility of high power cyclotrons - ScienceDirect
[13] Werner_Joho_Cyclotrons (psi.ch)
[14] Cyclotrons_Seidel_heraeus (gsi.de)
[15] Cyclotrons and Fixed-Field Alternating-Gradient Accelerators
[16] Phase compression-phase expansion effect

## Slide 27: RF acceleration
Depending on the concept, the constraints on RF acceleration differ considerably:
  Unlike cyclotrons, scaling FFAs operate like synchro-cyclotrons
  Beam stacking technique, harmonic number jump, serpentine acceleration are potential candidates
Coupled to the oscillating RF electric field, there is a time-varying magnetic field according to:
phase shift
The RF cavity causes orbit distortion  breakdown of the N-fold symmetry  resonances can be excited
As established by W. Joho [ref 16],
phase compression/phase expansion