## Slide 1
Production of radioisotopes for application studies at RIKEN RI Beam Factory
Nishina Center for Accelerator-Based Science, RIKEN
Hiromitsu Haba
1. Production of RIs at RIBF
2. Chemistry of Superheavy Elements
3. Targeted α-particle Therapy
4. Summary and Perspectives
CONTENTS

## Slide 2
1. Production of RIs at RIBF

## Slide 3
RIKEN
RIKEN Wako Campus (1967–)
RIBF
N
14 km to Olympic Stadium
RIKEN is Japan’s largest and most comprehensive research organization for basic and applied science.
Since 1917, RIKEN has fostered pioneering, innovative research in fields spanning the entire range of the natural sciences, from developmental biology and neuroscience to quantum physics and computer science.

## Slide 4
1937 Construction of 1st cyclotron
1938 Application of RIs as tracers for chemistry and biology
▪▪▪
2006 Construction of 7th – 9th cyclotrons → RIBF
RIKEN accelerators and RI application studies
Dr. Y. Nishina
(1890～1951)
1st
1937
8th
2006
2nd
1944
3rd
1952
4th
1966
RILAC2
2011
5th
1987
RILAC/
SRILAC
1981/2020
9th
2006
7th
2006
6th
1989
0 50 mm

## Slide 5
RRC
SRILAC
IRC
SRC
Acceleration of all ions up to 238U to 345 MeV/u (70% of c)
Production of RI beams in the whole mass region
BigRIPS
RRC
BigRIPS
+
AVF
RILAC2
fRC
AVF
SRILAC
RILAC2
+
RI Beam
RIKEN RI Beam Factory (RIBF)
Beam
Target
Slit
Superconducting Ring Cyclotron (SRC)
RI beam
Superconducting Ring Cyclotron (SRC)
RIs
Magnet
SC magnet
Energy (MeV/u)
Mass number
AVF + RRC + SRC
fRC
RRC
Energy for RI beam production
SRC
IRC
fRC
+
+
+
RI production

## Slide 6
AVF hot lab.
Facilities for production and application of RIs
AVF Cyclotron
RIKEN Ring Cyclotron
SC Heavy-ion Linac
Nucl. Chem. Lab.
Hot lab.
E3b
E7V
C03
GARIS I
GARIS III
E7b
RI Center

## Slide 7
(a) AVF Cyclotron
K70 AVF Cyclotron
12~30-MeV p (20 μA)
24-MeV d (15 μA)
29~50-MeV α (40 μA)
6~10-MeV 7Li, 11B, 12C, 18O, 19F, and 22Ne (1 pμA)
Production of 7Be (Z = 4) – 262Db (Z = 105)

## Slide 8
(a) AVF Cyclotron
K70 AVF Cyclotron
12~30-MeV p (20 μA)
24-MeV d (15 μA)
29~50-MeV α (32 μA)
6~10-MeV 7Li, 11B, 12C, 18O, 19F, and 22Ne (1 pμA)
Production of 7Be (Z = 4) – 262Db (Z = 105)
Short-lived RIs
Excitation function measurement
211At
SHE RIs

## Slide 9
Beams
(p, d, α, …)
TOF
0 50 mm
KCl
RI
Wobbler
Classical gas-jet method for RI production
Gas-jet method
1. No chemical separation
2. Short-lived RIs (T1/2 = ~1 s)
3. Thin-targets prepared by
vacuum evaporation and
electrodeposition
4. Stack of different targets
→ Multitracer
Cooling water
(1.5 L/min)
Thin targets for short-lived RIs
To Hot Lab.
Be foil (10 μm)
Ta beam stopper
Thick targets for long-lived RIs
He cooling gas (30 L/min)
Ta slit (φ9 mm)
He + KCl aerosol
(2 L/min)

## Slide 10
・Long-lived RIs
natTi, natAg, natHf, 197Au, and 232ThO2 (1–5 g/cm2) → Chemical separation
・Short-lived RIs
natCu, natAg, 197Au, natTa, and natPb (1–5 μm x 30) → Gas-jet transport
(b) RIKEN Ring Cyclotron (RRC)
Multitracer technology
RIs of a large number of elements are simultaneously produced from targets such as Ti, Ag, and Au irradiated with a 135 MeV/nucl. 14N (or 12C, 16O) beam from RRC [Ambe et al., Chem. Lett. 1991, 149 (1991). ]
.
K540 RIKEN Ring Cyclotron
Multitracer production chamber
135 MeV/nucl. 14N, 0.6 pμA
H. Haba et al., Radiochim. Acta 93, 539 (2005).

## Slide 11
γ-ray spectrum of the multitracer
Advantages of multitracer
• Multi-element analysis under an
identical experimental condition
• Rare RIs such as 28Mg, 42,43K, 47Ca, and 225Ac
• Useful for bio-trace element research
2 weeks after the irradiation
natAg(14N,xnyp)

## Slide 12
Focal plane
1
2 m
0
D2
Q2
Q1
D1
Rotating 248Cm target
Differential pumping section
Beam from RILAC
Beam dump
Gas inlet
Elastic scattering beam monitor
Evaporation Residues (ERs)
GAs-filled Recoil Ion Separator, GARIS
ERs
Mylar window
He(KCl)
0
100 mm
~0.1
kPa
~100 kPa
Gas-jet Transport System
Chemistry apparatus
D: Dipole magnet
Q: Quadrupole magnet
(c) RIKEN Liner Accelerator (RILAC)
GARIS
Gas-jet chamber
ERs
Superheavy elements (Z ≥ 104) for chemistry studies
RILAC
~7-MeV/u 18O, 19F, 22Ne, 23Na (3–7 pμA)

## Slide 13
RIKEN RIs for application studies

## Slide 14
AVF: Single RIs (7Be – 262Db)
RRC: Multitracer (7Be – 225Ac)
SRILAC: Superheavy elements (85Zr – 266Bh)
RI application studies in the fields of physics, chemistry, biology, engineering, medicine, pharmaceutical and environmental sciences
RIKEN Accelerator Progress Report
Sect. “Radiochemistry and Nuclear Chemistry”
http://www.rarf.riken.go.jp/researcher/APR/
RIKEN RIs for application studies

## Slide 15
FY2007 – FY2020
FY2016 – FY2020 from RIBF
Platform for short-lived RI distribution
Material Transfer Agreement
FY2019 –
FY2016 – FY2021, T. Nakano
Contribution to society through RI distribution
RIs | Orders | Users | Activity (MBq)
65Zn | 104 | 27 | 559.1
67Cu | 1 | 1 | 5
85Sr | 7 | 5 | 14.4
88Y | 13 | 2 | 12.03
109Cd | 36 | 15 | 214.15
Total | 161 | 50 | 804.68
RIs | Orders | Users | Activity (MBq)
7Be | 1 | 1 | 0.45
44mSc | 7 | 4 | 30
67Cu | 2 | 1 | 20
88Zr | 13 | 12 | 21
95Nb | 9 | 7 | 15
111Ag | 3 | 2 | 0.72
121mTe | 5 | 4 | 10
124Sb | 2 | 2 | 4
141Ce | 2 | 1 | 0.022
175Hf | 8 | 8 | 12
179Ta | 5 | 5 | 6
211At | 79 | 21 | 4,876
Total | 136 | 68 | 4,995.2
FY | RI | Orders | Activity (MBq)
2019 | 211At | 12 | 2,400
2020 | 211At | 16 | 3,200
Total |  | 28 | 5,600

## Slide 16
RIKEN RIs for application studies
211At
261Rfa,b, 262Db
265Sga,b, 266Bh

## Slide 17
2. Chemistry of Superheavy Elements

## Slide 18
70Zn
(Z = 30)
209Bi
(Z = 83)
279113
(Z = 113)
278113
Compound nucleus
Target
Projectile
Nuclear Fusion
Evaporation residue
Neutron
RILAC
Production of element 113 at RIBF
348-MeV 70Zn
(0.5 pμA x 553 days)
Z = 83 + 30
Cold fusion reaction of 209Bi(70Zn,n)278113
July 23, 2004
April 2, 2005
August 12, 2012
SF
SF
JPSJ 81, 103201 (2012).
JPSJ 76, 045001 (2007).
JPSJ 73, 2593 (2004).
σ = 22+20 fb
–13
Known isotopes

## Slide 19
Atomic number | Element name | Element symbol
113 | nihonium | Nh
115 | moscovium | Mc
117 | tennessine | Ts
118 | oganesson | Og
Nihonium – The first element discovered in Asian countries –
Naming ceremony in Tokyo, March 14, 2017

## Slide 20
Chemistry of new elements
• Chemical properties, periodicity, and electronic structure of new elements?
→ Verification of the influence of relativistic effects on chemical properties
→ Construction of ultimate atomic and molecular models
• Small cross sections (nb or pb) and short half-lives (< 1min)
→ Rapid and effective chemical experiments with “single atoms” at accelerators
1. Direct
Contraction of inner orbital (s, p)
2. Indirect
Expansion of outer orbital (d, f)
1–(v/c)2
0
a
me2
a
B
B
=
=
h2
m0
m
=
1–(v/c)2
Energy levels of valence electrons
Energy / eV
0
–2
–4
–6
–8
–10
–12
–14
–16
+
+
+
Hs
Os
Ru
nr
rel
nr
rel
nr
rel
5s1/2
4d5/2
4d3/2
4d
5s
6s1/2
5d5/2
5d3/2
5d
6s
7s1/2
6d5/2
6d3/2
6d
7s
The Chemistry of the Superheavy Elements,
M. Schädel (ed.), Kluwer Academic Publishers (2003).
+
Frontiers in chemistry
3. Spin orbit coupling

## Slide 21
Focal plane
1
2 m
0
D2
Q2
Q1
D1
Rotating 248Cm target
Differential pumping section
Beam from RILAC
Gas inlet
Elastic scattering beam monitor
Evaporation Residues (ERs)
GAs-filled Recoil Ion Separator, GARIS
ERs
Mylar window
He(KCl)
0
100 mm
~0.1
kPa
~100 kPa
Gas-jet Transport System
Chemistry apparatus
D: Dipole magnet
Q: Quadrupole magnet
RIKEN Liner Accelerator (RILAC)
GARIS
Gas-jet chamber
ERs
Superheavy elements (Z ≥ 104) for chemistry studies
RILAC
18O, 19F, 22Ne, and 23Na
(~7-MeV/u, 3–7 pμA)
Beam dump

## Slide 22
  Pre-separated SHE RIs are ready for chemistry experiments.
257No
24.5 s
8.69
(Iɑ = 20/80)
SF (≤ 51)
8.51
(18)
8.28,
SF (b < 13)
8.222 (Iɑ = 83), 8.323 (Iɑ = 17)
8.84 (Iɑ = 91/9), SF (b ≤ 50)
SF (82)
265Sg
8.5 s 14.4 s
261Rf
68 s 2.6 s
248Cm(22Ne,5n): 180/200 pb
248Cm(18O,5n): 12/11 nb
8.46 (Iɑ = 70), 8.68 (Iɑ = 30)
8.565 (Iɑ = 20), 8.595 (Iɑ = 46),
8.621 (Iɑ = 25), 8.654 (Iɑ = 9)
262Db
34 s
EC (b = 2.6)
SF (b = 52)
248Cm(19F,5n): 2.1 nb
258Lr
3.5 s
~5 h–1 (262Db)
~0.5 min–1 (261Rfa)
~1 h–1 (265Sga,b)
266Bh
10.0 s
248Cm(23Na,5n): 57 pb
8.62–9.40
~5 d–1 (266Bh)
Production and decay studies of 261Rf, 262Db, 265Sg, and 266Bh
  Haba et al., Chem. Lett. 38, 426 (2009).
  Haba et al., Phys. Rev. C 83, 034602 (2011).
  Haba et al., Phys. Rev. C 85, 024611 (2012).
  Murakami et al., Phys. Rev. C 88, 024618 (2013).
  Haba et al., Phys. Rev. C 89, 024618 (2014).
  Haba et al., Phys. Rev. C 102, 024625 (2020).

## Slide 23
GSI
J. Even et al., Science 345, 1491 (2014).
106Sg
42Mo
Group 6
5
6
7
74W
natZn(24Mg,xn)87,88Mo
144Sm(24Mg,xn)163,164W
248Cm(22Ne,5n)265Sga,b
• First organometallic compound of SHEs
Sg(0) – C chemical bonding
• Adsorption enthalpy (ΔHads) on SiO2
ΔHads(Sg) ≈ ΔHads(Mo) ≈ ΔHads(W)
Synthesis of carbonyl complexes of SHEs
Sg + 6CO → Sg(CO)6
CO collaboration: GSI, Mainz Univ., IMP, PSI, JAEA, …

## Slide 24
3. Targeted α-particle Therapy

## Slide 25
• Shorter range of α particle in tissue and higher LET than those of β particle
Particle | Energy (MeV) | Range in tissue (μm) | LET (keV/μm)
α | 5–9 | 40–100 | 60–80, 240
β | 0.05–2.3 | 50–1200 | 0.2
209Bi(α,2n)211At
Hermanne et al., Appl. Radiat. Isot. 63 (2005) 1.
210At (210Po)
211At
< 29 MeV
• High cytotoxicity and small influence for normal cell
Promising therapeutic RI for disseminated cancer, blood cancer, micro-metastatic cancer, …
211At for targeted α-particle therapy
211At
Cancer cell
Normal cell
β
α
211At
7.214 h
EC (58.2%)
211Po
0.516 s
207Pb
Stable
207Bi
31.55 y
α decay (41.8%)
Eα = 5.87 MeV
α decay (100%)
Eα = 7.45 MeV

## Slide 26
15o
Be vacuum window (20 μm)
Cooling He (30 L/min)
29-MeV α beam (40 μA)
209Bi target (M.P. 271.5oC)
(~75 mg/cm2)
Cooling water
(1.5 L/min, 10oC)
Development of production technology of 211At at AVF
Beam energy monitor
(TOF detector)
→ 29 (±1%) MeV
Beam wobbler
(2 Hz, φ3 mm)
40 μA×1 h → 1.3 GBq of 211At (EOB)
Al plate (1 mm)
H. Haba, Drug Delivery System 35, 114 (2020) (in JP).
AVF
29-MeV α
40 μA
Metallic 209Bi target
Chem. purity: 99.999%
Thickness: ~20 mg/cm2
46 mm
12 mm
850oC
PFA trap cooled with C2H5OH at –100 oC
Oxygen
200 μL of H2O, CH3OH, CHCCl3, …
(Chem. Yield: ~80%)
Water- and helium-cooled target chamber

## Slide 27
RIKEN RI platform for α-particle therapy
RIKEN Wako
Biofunctional Synthetic Chemistry Lab.
Lab. for Pathophysiological and Health Science
Lab. for Nonnatural Amino Acid Technology
Univ. Tokyo, School of Engineering
Tohoku Univ.
Hoshi Univ.
Fujifilm Toyama Chemical Co., Ltd.
Distribution of 211At (2016–)
17 users (July, 2021)
→ R&D for nuclear medicine
RIBF
Osaka Univ.
RIKEN Kobe
Kanazawa Univ.
QST Takasaki
Univ. Tokyo, Kavli IPMU
National Cancer Center Japan
Univ. Tokyo
Isotope Science Center
Hospital
Kindai Univ.
Under development
• 225Ac (2018–)
232Th(14N,xnyp)225Ac@RRC
226Ra(p,2n)225Ac@AVF with JRIA
• 212Pb (2017–)
212Pb generator with ATOX Co., Ltd.
(228Th→)224Ra→→→212Pb
Japan Radioisotope Association

## Slide 28
4. Summary and Perspectives
SRILAC
GARIS
AVF
Hot Lab.
Hot Lab.
SRC
BigRIPS
Production of >100 RIs for application studies at AVF, RRC, and SRILAC at RIKEN RIBF
•SHE chemistry: 261Rf, 262Db, 265Sg, and 267Bh
•Targeted α-particle therapy: 211At
RRC
Hot Lab.
RIKEN RIs
RI Center

## Slide 29
28 GHz ECRIS
GARIS III
–
Developments of large-scale RI production
Applications of SHE and medical RIs
RI production beam line under construction
SRILAC (Jan., 2020~)
Super-Conducting Quarter-Wavelength Resonator
Upgrade of RILAC for RI production
Medical RIs
SHE RIs
Nucl. Chem. Lab.
QWR

## Slide 30
28 GHz ECRIS
GARIS III
–
Developments of large-scale RI production
Applications of SHE and medical RIs
RI production beam line under construction
SRILAC (Jan., 2020~)
Super-Conducting Quarter-Wavelength Resonator
Upgrade of RILAC for RI production
Medical RIs
SHE RIs
Nucl. Chem. Lab.
QWR
• Large-scale production and stable supply of the short-lived 211At (T1/2 = 7.2 h) are important issues.
• Low-cost (construction and operation) cyclotrons, which can accelerate 30-MeV alpha particles with an intensity of >100 μA, would boost the 211At-therapy.
• Cyclotrons, which can accelerate various heavy ions (22Ne, 26Mg, 48Ca, 50Ti, 51V, …) with energies of ~7–10-MeV/u and intensities of ~10 pμA, are necessary for superheavy element researches.

## Slide 31
RIKEN Laboratories
Ion Source Team, Nishina Center
Super Heavy Element Group, Nishina Center
Next-generation Imaging Team
Biofunctional Synthetic Chemistry Laboratory
Domestic Universities and Institutes
Osaka University
Niigata University
Kanazawa University
Tohoku University
University of Tsukuba
Kyoto University
Okayama University
Hokkaido University
University of Tokyo
Tokyo Metropolitan University
Fukushima Medical University
International University of Health and Welfare
Hamamatsu Univ. School of Medicine
Suzuka Univ. of Medical Science
Hoshi University
Kindai University
Japan Atomic Energy Agency
Takasaki, National Institutes for Quantum and Radiological Science (QST)
RIKEN RI Collaboration
National Institute of Radiological Sciences, QST
National Cancer Center Japan
Oversea Universities and Institutes
Institute of Modern Physics
ATOMKI
Sunway University
Johannes Gutenberg University Mainz
Helmholtzzentrum für Schwerionenforschung GmbH
Helmholtz-Institut Mainz
Bern University
Paul Scherrer Institut
Saha Institute of Nuclear Physics
Umaru Musa Yar'adua University, Katsina
International Atomic Energy Agency
Public Interest Incorporated Association
Japan Radioisotope Association
Companies
Fujifilm Toyama Chemical Co., Ltd.
Metal Technology Co., Ltd.
ATOX Co., Ltd.
Chiyoda Technol Co., Ltd.
RIN Institute Inc.