## Slide 1
The Direct Injection System for the IsoDAR Cyclotron
Loyd Waites

## Slide 3: Innovation
Intense neutrino source requires intense proton source
10 mA beam current
  10X higher than commercial
Built underground, at a reasonable cost

## Slide 4: Three Paths to Higher Currents

## Slide 5: Use of H2+
High beam intensity + slow beam velocity
  Space charge ⇨ emittance growth
High impact of space charge in the low energy region
H2+: Two units of charge for one in the low energy region
Remove electron by stripping ⇨ two protons
https://arxiv.org/abs/1807.03759
Problem
Solution

## Slide 6: Experimental results
Currently Commissioning at 25% power
80% pure H2 +
High quality beam emittance: 0.05 π-mm-mrad (RMS, norm.)
Currently working to increase power
https://arxiv.org/abs/2008.12292

## Slide 7: RFQ injection
Replaces large LEBT
Bunching allows for higher phase acceptance
Significantly higher transmission
RFQ-DIP
https://aip.scitation.org/doi/abs/10.1063/1.4935753 https://arxiv.org/abs/1807.03759

## Slide 8
LEBT diagnostics
Radio-Frequency Quadrupole (RFQ)
Electrostatic LEBT
MIST-1 Ion Source
System Overview:
https://arxiv.org/abs/1807.03759
https://aip.scitation.org/doi/abs/10.1063/1.4935753

## Slide 9: Particles are continuously focused transversally, while being bunched longitudinally
Highly accurate particle in cell (PIC) simulations using well-established WARP code

## Slide 10: Vortex Motion

## Slide 11: Vortex Motion
Trans.
Long.

## Slide 12: Vortex Motion
Courtesy of Wiel Kleeven (Cyclotrons 2016)

## Slide 13: PSI Injector II
Vortex motion effect experimentally observed in PSI Injector II
OPAL simulations with space charge matched experimental results
OPAL simulations see similar result in IsoDAR
Turn 0
Turn 5
Turn 10
Turn 20
Turn 30
Turn 40
https://journals.aps.org/prab/abstract/10.1103/PhysRevSTAB.13.064201

## Slide 14
With Space Charge
Without Space Charge

## Slide 15
With Space Charge
Without Space Charge

## Slide 16: We performed highly accurate PIC simulations of our cyclotron design
https://arxiv.org/abs/2103.09352
In IsoDAR the halo is removed with collimators
Beam forms stable, round distribution (vortex) after 6 turns
Start
7 Turns, no coll.
7 Turns, 12 coll.
7 Turns, no coll. No SC
Notes: Beam stays in this nice round shape for another 100 turns until energy has reached 60 MeV/amu

## Slide 17: Beam can be extracted with good quality
Minimal losses at 60 MeV/amu: ~ 100 Watts
RMS Size:
  Vertical: 7.5 mm
  Longitudinal: 11 mm
  Vertical: 1.9 mm
RMS, normalized emittance:
  vertical: 0.44 mm-mrad
  Radial: 3.8 mm-mrad
Longitudinal emittance:
  0.1 MeV-deg
https://arxiv.org/abs/2103.09352
Notes: Beam can be split off nicely and then be guided through the yoke out of the cyclotron. There, we strip away the electron and transport 10 mA of protons to the target.

## Slide 18: Conclusions
The IsoDAR cyclotron leverages new developments in accelerator technology to push the limits of beam power from a compact system, leading to exciting applications in neutrino physics.