## Slide 1: DAQ + SlowCtrl status

## Slide 2
Status 6/30 9:24 am
i.e., outdated.

## Slide 3
Overview of DAQ system
FE: GEM left
[on vme-left.dl]
FE: GEM right
[on vme-right.dl]
FE: Trigger
[on dltdc.dl]
MIDAS server
SlowCtrl
DLFridge
ROOT Files
Online Analysis with Visual Cooker (visco)
Note: No mhttp, no mlogger. No midasconverter. The ROOT files can be analyzed by visco while being written. Please provide a variant of your plugins that only need one pass.

## Slide 4
Overview of SlowCtrl system
Most power supplies, hall probe
Jaya gateway for beam line variables
ODB gateway
EPICS server
Web App
Postgres SQL DB
DLFridge

## Slide 5
Where is stuff? Servers [A/Cd hut on the roof]
dl-server-1.triumf.ca / dl-server-1.dl
Cores for slurm tasks
1 gig to TRIUMF, 10gig to our network
dl-server-2.triumf.ca / dl-server-2.dl
All services
  mserver
  PostgreSQL
  DLFridge
  Elog
  Slowctrl-web
  Home dirs
  LDAP
Cores for slurm tasks
1 gig to TRIUMF, 10gig to our network
Clusterswitch.dl
2x10Gig bonded link to rackswitch.dl

## Slide 6
Where is stuff? Rack (on the roof)
Gemlv.dl
APV low voltage supply
vme-left.dl
MPDs For beam-left GEMs
HV?
Space for Trigger electronics
Rackswitch.dl
Hall-left.dl and hall-right.dl [behind]
Field/temperature measurement
vme-right.dl
MPDs For beam-right GEMs
HV?
dipole-left.dl
Dipole power for beam-left spectrometer
dipole-right.dl
Dipole power for beam-left spectrometer

## Slide 7
Where is stuff? Counting room
dl-daq-1.triumf.ca / dl-daq-1.dl
For online analysis
dl-daq-2.triumf.ca / dl-daq-2.dl
For slowctrl

## Slide 8
Accounts and stuff
All accounts have a shared home
  Please be considerate how much you write to home – it’s a shared 4TB disk, and it also contains the database
Special accounts
  dlcluster
    This will run analysis jobs for near-online analysis via slurm
    Also
  daq
    Runs mserver, dlfridge and the frontends
  Slowctrl
    Runs slow ctrl web app, epics

## Slide 9
Passwords
For dl-daq-1 and dl-daq-2:
  User is dl1 and dl2.
  Password is …
For slowctrl web user:
  Use slowctrl and pw ….
  Without this, you can only view things
  With it, you can change things.

## Slide 10
NB.:
    Only dl-server-* and dl-daq-* are in the TRIUMF network.
      Local systems / internal network is separate, “dl” domain
    From TRIUMF, you can access them from your computer, but it’s not automatic:
      You need to set a network route to 192.168.17.x via gateway dl-server-2.triumf.ca
      You need to set your DNS server to dl-server-2.triumf.ca
      No, I cannot make that easier
    Services are reachable via:
      Slowctrl.dl = dl-server-2.triumf.ca/slowctrl
      Elog.dl = dl-server-2.triumf.ca/elog

## Slide 11
A tour of the slow ctrl: DAQ

## Slide 12
A tour of the slow ctrl: DAQ (zoom)

## Slide 13
https://dlshifts.cfnssbu.physics.sunysb.edu/

## Slide 14
Open questions/tasks
Control of Trigger PS
What to do with Trigger scaler
  Only in SlowCtrl?
  Also in the root file? How synchronized?
Does GEM readout work?
Does sync work?
One GEM HV seems broken? Works in the beginning, but disconnects from bus after a while
Lower crate controller locks up when connected to network
Pressures from BL
Second PPG32
GEM zero suppression on FE or in DLFridge possible?
Magnet power + interlock test
Add trigger config to slowctrl