## Slide 1
Recent Progress
Mosaix Probe Card – V0 Expected delivery tomorrow at CERN, cables and hardware necessary to connect it to the Testing setup are ready Some FPC expected from the PCB workshop tomorrow – ready to test on Monday probably
Mosaix Probe Card – V1 FPC only Proposal draft design for MPI completed and sent Monday 2nd of March – waiting for a feedback Pros: Minimized interconnects for better signal integrity, easier handling of the cables outside the WP (could be important when testing multiple MOSAIX in parallel!) Cons: Fabrication and Assembly might be technologically challenging, MPI feedback is needed
Initial testing of ER2 in DSF, to be continued Operation on the machine is still done manually – supporting ITS3 team for reliable wafer contact Planning to test WP SW automation procedures in the next weeks with Angelina (she’ll be here until March 18th )
SVT SW on WP Agent Discussions ongoing with Angelina, Ivan, Sasha on the communication between software agents, Implementation and debugging foreseen as main activity in the next 2 weeks (as well as high speed links tests)
Probe Card FPCs - PCBs ITS3 PCB necessary to observe High Speed links on the oscilloscope is suboptimal (we think) but in hand We could design and submit our own improved version – low priority for now