## Slide 1
The IDEA detector concept
Paolo Giacomelli
INFN Bologna
These projects have received funding from the European Union’s Horizon Europe Research and Innovation programme under Grant Agreements No. 101004761 (AIDAinnova), 101057511 (EURO-LABS).

## Slide 2: The IDEA detector concept
New, innovative, possibly more cost-effective concept
  Silicon vertex detector
  Short-drift, ultra-light wire chamber
  Dual-readout calorimeter
  Thin and light solenoid coil inside calorimeter system
    Small magnet ⇒ small yoke
  Muon system made of 3 layers of m-RWELL detectors in the return yoke
https://pos.sissa.it/390/
IDEA concept (proposed in FCC CDR)
Innovative Detector for e+e- Accelerator
Acknowledgments
I need to thank many colleagues, in particular:
F. Bedeschi

## Slide 3: IDEA detector layout
Beam pipe: R∼1.0 cm
Vertex:
5 MAPS layers
R = 1.37-31.5 cm
Drift Chamber: 112 layers
4 m long, R = 35-200 cm
Outer Silicon wrapper:
Si strips
Superconducting solenoid coil:
2 T, R ∼ 2.1-2.4 m
0.74 X0, 0.16 l @ 90°
Preshower: ∼1 X0
Dual-Readout Calorimeter:
2m / 7 lint
Yoke + Muon chambers

## Slide 4: Vertex detector: IDEA
Outer vertex tracker:
Modules of pixel size
Intermediate barrel at 13 cm radius (improved reconstruction for)
Outer barrel at 31.5 cm radius
3 disks per side
Inner Vertex detector:
Modules of pixel size
3 barrel layers at
13.7, 22.7 and 34.8 mm radius
Mid-term review vertex detector overall layout
F. Palla

## Slide 5: Vertex detector: IDEA
  Inner Vertex (ARCADIA based):
    Lfoundry 110 nm process
    50 µm thick
    Dimensions:
    Power density 30 mW/cm2
    100 MHz/cm2
  Outer Vertex and disks (ATLASPIX3 based)
    TSI 180 nm process
    50 µm thick
    Module dimensions:
    Power density 170 mW/cm2
    Up to 1.28 Gb/s downlink
Power
Data IN/OUT
HV
Depleted Monolithic Active Pixel Detectors
F. Palla
See talk by F. Palla for more details on the vertex tracker

## Slide 6: Vertex detector mechanical integration
Vertex design based on:
  ARCADIA inner 3 layers
    Air cooled
  AtlasPix3 outer 2 layers/disks
    Liquid cooled
Layer 1
Outer layer

## Slide 7: Vertex detector: IDEA
General integration
F. Palla

## Slide 8: Vertex detector: IDEA
C. Turrioni

## Slide 9: Momentum measurement
ZH (Hmm)
Muon pt
ZH (Hmm)
Muon pt
90 degree
MS only
ZH (Zmm)
Muon pt
Z or H decay muons in ZH events have rather low pt
  Transparency more important than asymptotic resolution

## Slide 10: Drift chamber
IDEA DC
IDEA: Extremely transparent Drift Chamber
  Gas: 90% He – 10% iC4H10
  Radius 0.35 – 2.00 m
  Total thickness: 1.6% of X0 at 90o
  All stereo wires (56448 cells, 343968 wires)
    Tungsten wires dominant contribution
  112 layers for each 15o azimuthal sector
  max drift time: 350 ns
L = 4m

## Slide 11: Drift chamber
Gas envelope
Wire Cage
Based on MEG2 experience
Based on MEG2 experience
90% He - 10% C4H10 – All stereo – s ~ 100 mm
Small cells, max drift time ~ 350 ns

## Slide 12: Drift chamber
dN/dx from Garfield++
In general, tracks have rather low momenta (pT ≲ 50 GeV)
  Transparency more relevant than asymptotic resolution
Drift chamber (gaseous tracker) advantages
  Extremely transparent: minimal multiple scattering and secondary interactions
  Continuous tracking: reconstruction of far-detached vertices (K0S , L, BSM, LLPs)
  Outstanding Particle separation via dE/dx or cluster counting (dN/dx)
    >3s K/p separation up to ~35 GeV

## Slide 13: Cluster counting
Test beam data 2022
Cluster counting 2x better than dE/dx
  Poisson vs . Landau  no large tails
Sample signal few GHz  on detector electronics R&D

## Slide 14: Drift chamber future plans
Complete mapping of dN/dx data in all relevant bg regions (few years)
  Understand details of cluster counting performance
Build large mechanical prototype (few years)
Build full length functioning prototype with few cells (few years)
Develop on-detector cluster counting electronics (few years)
Towards a drift chamber TDR

## Slide 15: Resistive LGAD
Very attractive option for timing in Si wrapper region
Cost reduction is major area of R&D
Some “fast” devices also prototyped by Arcadia group
Recent new activity with INFN-GE/(TO)
  Match time and position resolution

## Slide 16: Superconducting solenoid
Courtesy of H. TenKate
Ultra light 2 T solenoid:
  Radial envelope 30 cm
  Single layer self-supporting winding (20 kA)
    Cold mass: X0 = 0.46, λ = 0.09
  Vacuum vessel (25 mm Al): X0 = 0.28
    Can improve with new technology
      Corrugated plate: X0 = 0.11
      Honeycomb: X0 = 0.04
Interest from Genova (in synergy with DUNE) on alternative superconducting magnets like MgB2

## Slide 17: Dual Readout Calorimetry
Alternate
Cherenkov fibers
Scintillating fibers
with:
Newer DR calorimeter
( bucatini calorimeter)
~2m long capillaries
Measure simultaneously:
  Scintillation signal (S)
  Cherenkov signal (Q)
Calibrate both signals with e-
Unfold event by event fem to obtain corrected energy

## Slide 18: Dual Readout Calorimeter
Full GEANT4 implementation of the DR calorimeter
EM
HAD

## Slide 19: DR calorimeter
Absolute calibration in ph.e
International collaboration:
  TTU (USA), Sussex (UK), several universities (Korea – 2 M$/5 yr), Chile
  Princeton, Maryland (USA), CERN for crystal extension
EM prototype built and tested on beams (DESY/CERN)

## Slide 20: DR calorimeter
Full containment hadronic prototype in progress
  Hidra2 call INFN CSN5

## Slide 21: Dual readout future plans
Complete construction/test of Hidra2 prototype (one year)
  Demonstrate resolution with full containment
Develop scalable readout electronics (few years)
Optimize metal matrix mechanics for large production (few years)
Develop mechanical model of full system with services (few years)
Towards a DR calorimeter TDR

## Slide 22: Crystal option

## Slide 23: Crystal option
ECAL layer:
  PbWO crystals
  front segment 5 cm (~5.4 X0)
  rear segment for core shower
  (15 cm ~16.3 X0)
  10x10x200 mm³ of crystal
  5x5 mm² SiPMs (10-15 um)
1x1x5 cm3
PbWO
1x1x15 cm3
PbWO
~20 cm PbWO4
sEM ≈ 3%/
DR w. filters
Timing layer
  LYSO 20-30 ps
PF for jets

## Slide 24: Crystal option future plans
Optimize crystal choice (few years)
Develop scalable readout electronics (few years)
Re-optimize fiber DR calorimeter (few years)
Develop mechanical model of full system with services (few years)
Towards an EM calorimeter TDR

## Slide 25: m-RWELL technology
The m-RWELL is composed of only two elements:
m-RWELL_PCB
drift/cathode PCB defining the gas gap
m-RWELL_PCB = amplification-stage ⊕ resistive stage ⊕ readout PCB
m-RWELL operation:
  A charged particle ionises the gas between the two detector elements
  Primary electrons drift towards the m-RWELL_PCB (anode) where they are multiplied, while ions drift to the cathode
  The signal is induced capacitively, through the DLC layer, to the readout PCB
  HV is applied between the Anode and Cathode PCB electrodes
  HV is also applied to the copper layer on the top of the kapton foil, providing the amplification field
(*) G. Bencivenni et al., “The micro-Resistive WELL detector: a compact spark-protected single amplification-stage MPGD”, 2015_JINST_10_P02008)
LNF
BOLOGNA
FERRARA
TORINO

## Slide 26: Preshower and muon detector
Preshower Detector
High resolution after the magnet
to improve p±/e± and 2g separation
Efficiency > 98%
Space Resolution < 100 mm
Mass production
Optimization of FEE channels/cost
Muon Detector
Identify muons and search for LLPs
Efficiency > 98%
Space Resolution < 400 mm
Mass production
Optimization of FEE channels/cost
Preshower
pitch = 0.4 mm
FEE capacitance = 70 pF
1.3 million channels
Muon
pitch = 1.2 mm
FEE capacitance = 220 pF
5 million channels
Barrel Preshower
Similar design for the Muon detector
Endcap Preshower
Similar design for the Muon detector
50x50 cm2 2D tiles to cover more than 1650 m2
Detector technology: µ-RWELL

## Slide 27: Ongoing R&D Click here for more R&D information

## Slide 28: ARCADIA MD3 test
110 nm CMOS CIS technology, high-resistivity bulk, operated in full depletion mode
3 engineering runs with:
  full-scale DMAPS
  sensor R&D (monolithic FD-strips and readout, fast sensors with gain layer)
High rate capability (100 MHz/cm2) architecture on a scalable 512x512 pixel matrix (25 mm pitch) MD3 Main Demonstrator chip:
  measured 30 mW/cm2 at full-speed (16 data Tx active) and 10 mW/cm2 on low-rate mode (1 data Tx active)
Main Demonstrator
MD3
Matrix: 1,28 x 1,28 cm2
Cosmic ray data

## Slide 29: Silicon detectors: ATLASPix3
Based on ATLASPIX3 R&D
  50x50 mm2
  Up to 1.28 Gb/s downlink
  TSI 180 nm process
  132 columns of 372 pixels
Active length (r-phi x z)
  18.6 mm x 19.8 mm
Module is made of 2x2 chips
Power goal 100 mW/cm2 (175 now)

## Slide 30: 2020 Dual Readout prototype
Electromagnetic dimensions of 10x10x100 cm3
9 towers containing 16x20 capillaries (160 C and 160 S)
Capillary tube with outer diameter of 2 mm and inner diameter of 1.1 mm 1-mm-thick fibers
Full prototype - 9 towers
Single tower
Fiber guiding system
Hamamatsu SiPM: S14160-1315
PS Cell size: 15 μm
Front end board
housing 64 SiPM
Readout Boards CAEN A5202
“Bucatini calorimeter”

## Slide 31: Crystal ECAL with DR calorimeter
M. Lucchini

## Slide 32: Crystal ECAL with DR calorimeter
Sensible improvement in jet resolution using dual-readout information combined
with a particle flow approach → 3-4% for jet energies above 50 GeV
crystals + IDEA w/o DRO
crystals + IDEA w/ DRO
crystals + IDEA w/ DRO + pPFA
Event display
M. Lucchini

## Slide 33: m-RWELL: Test beam 2021
New μ-RWELL prototypes with 40 cm long strips
strips
beam
7 m-RWELL prototypes with resistivity varying between
10 and 80 MOhm/£
will allow to define best resistivity for final 50x50 cm2 detector
H8 Test beam 11/2021
a) Design optimization:
- different HV filter applied
b) Detector characterization
- HV scan at 0°
- HV scan at different angles and drift field
1- Signal shape
(cluster charge, cluster size)
2 - Detector performance
(efficiency, space resolution)
LNF
BOLOGNA
FERRARA
TORINO

## Slide 34: Muon and pre-shower future plans
Complete test of large 2D chamber design (50x50 cm2) (this year)
Complete readout electronics based on TIGER chip (next years)
Develop chamber production plan with industry (few years)
Develop plan for layout on detector with services (few years)
Towards a Muon/pre-shower TDR

## Slide 35: Status of Simulation of IDEA concept
FASTSIM Delphes IDEA card used for performance studies FCCSW
Very sophisticated compared to default.
Latest additions: Vertexing, LLP, PID, dN/dx, dE/dx
FULLSIM: standalone GEANT4 description
Fully integrated geometry
Output hits and reco tracks converted to EDM4HEP
Ready for PFlow development and other reconstruction frameworks/algorithms (ACTS, Pandora etc) in FCCSW

## Slide 36: Some considerations
The IDEA detector concept was originally conceived by several Italian groups
  Clearly if this detector will be built, it will have to be by a large international collaboration
    US could provide a fundamental contribution to several areas:
      Silicon detectors: silicon sensors, readout electronics, mechanics
      Wire chamber: lots of expertise available in the US
      DR calorimeter, and in particular the EM crystal DR calorimeter: lots of past experience from CMS, etc.
      Other areas (Simulation, DAQ&Trigger, software, etc.) ...
      There are already collaborations FNAL/Padova on ARCADia and CalVision on DR calorimetry

## Slide 37: Some more considerations
The IDEA detector is also well represented in the largest EU-funded project on detectors R&D for particle physics: AIDAinnova
  AIDAinnova ends on 31/03/2025 but is actively looking at a new call to continue its activities: IDEA would be again largely present and financed, there is space for collaboration with US groups
    US groups can participate in another EU-funded project that provides Transnational Access to test beams and irradiation facilities in more than 40 European Research Infrastructures, EURO-LABS
      EURO-LABS allows up to 20% of its funding to go to non-EU research groups
    We have excellent connections with AIDAinnova and EURO-LABS (P.G. is the PI of both projects...)

## Slide 38: Conclusions
FCC-ee will be a fascinating machine, allowing to achieve unprecedented precision on EW measurements and Higgs couplings
  The IDEA detector concept could be an excellent choice for one of the IPs
    Very good momentum measurement
    Outstanding PID with cluster counting from the drift chamber
    Excellent calorimetry
    Precise and efficient muon detector
    Very appealing upgrade options! (DR EM crystal calorimeter, LGADs for the Si wrapper)
Need for significant R&D in the next 4-5 years
  A lot of ongoing activities on all IDEA sub-detectors
  Profiting from several national funding schemes, EU projects, etc.
  INFN was central in all these R&D activities and started many of them
  Now several international colleagues have joined these efforts
Lots of possibilities for US colleagues to join IDEA and help on all these developments!!

## Slide 39: Backup

## Slide 40: Vertex inner barrel
A. Ilg

## Slide 41: Vertex outer barrel
A. Ilg